DMX Channel Table

| 3Ch mode |
| --- |
| Ch. | Function | Values | Sub-group |
| 1 | Zoom | 000 | - | 255 | 0%-100% | Zoom |
| 2 | Dimmer | 000 | - | 255 | 0%-100% | Dimmer |
| 3 | Colour Macro (override RGBW) | 000 | - | 005 | Colour OFF | Colour Macro |
|  |  | 006 | - | 013 | Red |  |
|  |  | 014 | - | 021 | Amber |  |
|  |  | 022 | - | 029 | Yellow Amber |  |
|  |  | 030 | - | 037 | Yellow |  |
|  |  | 038 | - | 045 | Green |  |
|  |  | 046 | - | 053 | Turquoise |  |
|  |  | 054 | - | 061 | Cyan |  |
|  |  | 062 | - | 069 | Blue |  |
|  |  | 070 | - | 077 | Lavender |  |
|  |  | 078 | - | 085 | Mauve |  |
|  |  | 086 | - | 093 | Magenta |  |
|  |  | 094 | - | 101 | Pink |  |
|  |  | 102 | - | 109 | Warm White |  |
|  |  | 110 | - | 117 | White |  |
|  |  | 118 |  | 125 | Cold White |  |
|  |  | 126 |  | 127 | Colour jumping stop |  |
|  |  | 128 |  | 191 | Colour jumping Speed slow->fast/Colour1->12 |  |
|  |  | 192 |  | 255 | Colour fading Speed slow->fast/Colour1->12 |  |

| 4Ch mode1 |
| --- |
| Ch. | Function | Values | Sub-group |
| 1 | Zoom | 000 | - | 255 | 0%-100% | Zoom |
| 2 | Dimmer | 000 | - | 255 | 0%-100% | Dimmer |
| 3 | Strobe | 000 | - | 005 | Strobe Open | Strobe |
|  |  | 006 | - | 010 | Strobe Close |  |
|  |  | 011 | - | 250 | Strobe slow->fast<1Hz-20Hz |  |
|  |  | 251 | - | 255 | Strobe Open |  |
| 4 | Colour Macro (override RGBW) | 000 | - | 005 | Colour OFF | Colour Macro |
|  |  | 006 | - | 013 | Red |  |
|  |  | 014 | - | 021 | Amber |  |
|  |  | 022 | - | 029 | Yellow Amber |  |
|  |  | 030 | - | 037 | Yellow |  |
|  |  | 038 | - | 045 | Green |  |
|  |  | 046 | - | 053 | Turquoise |  |
|  |  | 054 | - | 061 | Cyan |  |
|  |  | 062 | - | 069 | Blue |  |
|  |  | 070 | - | 077 | Lavender |  |
|  |  | 078 | - | 085 | Mauve |  |
|  |  | 086 | - | 093 | Magenta |  |
|  |  | 094 | - | 101 | Pink |  |
|  |  | 102 | - | 109 | Warm White |  |
|  |  | 110 | - | 117 | White |  |
|  |  | 118 |  | 125 | Cold White |  |
|  |  | 126 |  | 127 | Colour jumping stop |  |
|  |  | 128 |  | 191 | Colour jumping Speed slow->fast/Colour1->12 |  |
|  |  | 192 |  | 255 | Colour fading Speed slow->fast/Colour1->12 |  |

| 4Ch mode2 |
| --- |
| Ch. | Function | Values | Sub-group |
| 1 | Zoom | 000 | - | 255 | 0%-100% | Zoom |
| 2 | Red | 000 | - | 255 | Red 0%-100% | Red |
| 3 | Green | 000 | - | 255 | Green 0%-100% | Green |
| 4 | Blue | 000 | - | 255 | Blue 0%-100% | Blue |

| 5Ch mode |
| --- |
| Ch. | Function | Values | Sub-group |
| 1 | Zoom | 000 | - | 255 | 0%-100% | Zoom |
| 2 | Red | 000 | - | 255 | Red 0%-100% | Red |
| 3 | Green | 000 | - | 255 | Green 0%-100% | Green |
| 4 | Blue | 000 | - | 255 | Blue 0%-100% | Blue |
| 5 | White | 000 | - | 255 | White 0%-100% | Whtie |
| 15Ch mode |
| Ch. | Function | Values | Sub-group |
| 1 | Zoom | 000 | - | 255 | 0%-100% | Zoom |
| 2 | Dimmer | 000 | - | 255 | Red 0%-100% | Dimmer |
| 3 | Strobe functions | 000 | - | 005 | Strobe open | Multifunctional-strobe |
|  |  | 006 | - | 010 | Strobe closed |  |
|  |  | 011 | - | 250 | Strobe slow -> fast <1Hz - 20Hz |  |
|  |  | 251 | - | 255 | Strobe open |  |
| 5 | Red | 000 | - | 255 | Red 0%-100% | Red |
| 5 | Green | 000 | - | 255 | Green 0%-100% | Green |
| 6 | Blue | 000 | - | 255 | Blue 0%-100% | Blue |
| 7 | White | 000 | - | 255 | White 0%-100% | White |
| 8 | Colour Macro (override RGBW) | 000 | - | 005 | Colour OFF | Colour Macro |
|  |  | 006 | - | 013 | Red |  |
|  |  | 014 | - | 021 | Amber |  |
|  |  | 022 | - | 029 | Yellow Amber |  |
|  |  | 030 | - | 037 | Yellow |  |
|  |  | 038 | - | 045 | Green |  |
|  |  | 046 | - | 053 | Turquoise |  |
|  |  | 054 | - | 061 | Cyan |  |
|  |  | 062 | - | 069 | Blue |  |
|  |  | 070 | - | 077 | Lavender |  |
|  |  | 078 | - | 085 | Mauve |  |
|  |  | 086 | - | 093 | Magenta |  |
|  |  | 094 | - | 101 | Pink |  |
|  |  | 102 | - | 109 | Warm White |  |
|  |  | 110 | - | 117 | White |  |
|  |  | 118 |  | 125 | Cold White |  |
|  |  | 126 |  | 127 | Colour jumping stop |  |
|  |  | 128 |  | 191 | Colour jumping Speed slow->fast/Colour1->12 |  |
|  |  | 192 |  | 255 | Colour fading Speed slow->fast/Colour1->12 |  |
| 9 | Dimmer Curve | 000 | - | 005 | No function | Set dimmer curve |
|  |  | 006 | - | 063 | Linear Dimmer Curve |  |
|  |  | 064 | - | 127 | Exponential Dimmer Curve |  |
|  |  | 128 | - | 191 | Logarithmic Dimmer Curve |  |
|  |  | 192 | - | 255 | S-Curve Dimmer Curve |  |
| 10 | Device settings | 000 | - | 005 | No function | Device settings |
|  |  | 006 | - | 055 | Dimmer Response LED (Hold 3s) |  |
|  |  | 056 | - | 105 | Dimmer Response Halogen (Hold 5s) |  |
|  |  | 106 | - | 155 | Setting Fan High Mode (Hold 3s) |  |
|  |  | 156 | - | 205 | Setting Fan Auto Mode (Hold 3s) |  |
|  |  | 206 | - | 255 | Reset All Function(Hold 5s) |  |
| 11 | Ground Colour Dimmer | 000 | - | 255 | Ground Colour Dimmer 0%-100% | Ground Colour Dimmer |
| 12 | Ground Colour Strobe | 000 | - | 255 | Ground Colour Strobe slow->fast<1-20HZ | Ground Colour Strobe |
| 13 | Ground Colour Red | 000 | - | 255 | Ground Colour Red 0%-100% | Ground Colour Red |
| 14 | Ground Colour Green | 000 | - | 255 | Ground Colour Green 0%-100% | Ground Colour Green |
| 15 | Ground Colour Blue | 000 | - | 255 | Ground Colour Blue 0%-100% | Ground Colour Blue |

| 20Ch mode |
| --- |
| Ch. | Function | Values | Sub-group |
| 1 | Zoom | 000 | - | 255 | 0%-100% | Zoom |
| 2 | Red1 | 000 | - | 255 | Red1 0%-100% | Red1 |
| 3 | Green1 | 000 | - | 255 | Green1 0%-100% | Green1 |
| 4 | Blue1 | 000 | - | 255 | Blue1 0%-100% | Blue1 |
| 5 | White1 | 000 | - | 255 | White1 0%-100% | Whtie1 |
| 6 | Red2 | 000 | - | 255 | Red2 0%-100% | Red2 |
| 7 | Green2 | 000 | - | 255 | Green2 0%-100% | Green2 |
| 8 | Blue2 | 000 | - | 255 | Blue2 0%-100% | Blue2 |
| 9 | White2 | 000 | - | 255 | White2 0%-100% | Whtie2 |
| 10 | Red3 | 000 | - | 255 | Red3 0%-100% | Red3 |
| 11 | Green3 | 000 | - | 255 | Green3 0%-100% | Green3 |
| 12 | Blue3 | 000 | - | 255 | Blue3 0%-100% | Blue3 |
| 13 | White3 | 000 | - | 255 | White3 0%-100% | Whtie3 |
| 14 | Red4 | 000 | - | 255 | Red4 0%-100% | Red4 |
| 15 | Green4 | 000 | - | 255 | Green4 0%-100% | Green4 |
| 16 | Blue4 | 000 | - | 255 | Blue4 0%-100% | Blue4 |
| 17 | White4 | 000 | - | 255 | White4 0%-100% | Whtie4 |
| 18 | Ground Colour Red | 000 | - | 255 | Ground Colour Red 0%-100% | Ground Colour Red |
| 19 | Ground Colour Green | 000 | - | 255 | Ground Colour Green 0%-100% | Ground Colour Green |
| 20 | Ground Colour Blue | 000 | - | 255 | Ground Colour Blue 0%-100% | Ground Colour Blue |
| 21Ch mode |
| Ch. | Function | Values | Sub-group |
| 1 | Zoom | 000 | - | 255 | 0%-100% | Zoom |
| 2 | Zoom speed | 000 | - | 255 | Fast->Slow | Zoom speed |
| 3 | Dimmer | 000 | - | 255 | 0%-100% | Dimmer |
| 4 | Strobe functions | 000 | - | 005 | Strobe open | Green |
|  |  | 006 | - | 010 | Strobe closed | Multifunctional-strobe |
|  |  | 011 | - | 033 | Plus Random, slow->fast |  |
|  |  | 034 | - | 056 | Ramp up Random, slow -> fast |  |
|  |  | 057 | - | 079 | Ramp down Random, slow -> fast |  |
|  |  | 080 | - | 102 | Random Strobe Effect, slow -> fast |  |
|  |  | 103 | - | 127 | Strobe Break Effect, 5s…..1s (Short burst with break) |  |
|  |  | 128 | - | 250 | Strobe slow -> fast <1Hz - 20Hz |  |
|  |  | 251 | - | 255 | Strobe open |  |
| 5 | Red | 000 | - | 255 | Red 0%-100% | Red |
| 6 | Green | 000 | - | 255 | Green 0%-100% | Green |
| 7 | Blue | 000 | - | 255 | Blue 0%-100% | Blue |
| 8 | White | 000 | - | 255 | White 0%-100% | White |
| 9 | Colour Macro (override RGBW) | 000 | - | 005 | Colour OFF | Colour Macro |
|  |  | 006 | - | 013 | Red |  |
|  |  | 014 | - | 021 | Amber |  |
|  |  | 022 | - | 029 | Yellow Amber |  |
|  |  | 030 | - | 037 | Yellow |  |
|  |  | 038 | - | 045 | Green |  |
|  |  | 046 | - | 053 | Turquoise |  |
|  |  | 054 | - | 061 | Cyan |  |
|  |  | 062 | - | 069 | Blue |  |
|  |  | 070 | - | 077 | Lavender |  |
|  |  | 078 | - | 085 | Mauve |  |
|  |  | 086 | - | 093 | Magenta |  |
|  |  | 094 | - | 101 | Pink |  |
|  |  | 102 | - | 109 | Warm White |  |
|  |  | 110 | - | 117 | White |  |
|  |  | 118 |  | 125 | Cold White |  |
|  |  | 126 |  | 127 | Colour jumping stop |  |
|  |  | 128 |  | 191 | Colour jumping Speed slow->fast/Colour1->12 |  |
|  |  | 192 |  | 255 | Colour fading Speed slow->fast/Colour1->12 |  |
| 10 | Rainbow | 000 | - | 005 | Rainbow off | Rainbow effect |
|  |  | 006 | - | 021 | Rainbow1 |  |
|  |  | 022 | - | 037 | Rainbow2 |  |
|  |  | 038 | - | 053 | Rainbow3 |  |
|  |  | 054 | - | 069 | Rainbow4 |  |
|  |  | 070 | - | 085 | Rainbow5 |  |
|  |  | 086 | - | 101 | Rainbow6 |  |
|  |  | 102 | - | 117 | Rainbow7 |  |
|  |  | 118 | - | 133 | Rainbow8 |  |
|  |  | 134 | - | 149 | Rainbow9 |  |
|  |  | 150 | - | 165 | Rainbow10 |  |
|  |  | 166 | - | 181 | Rainbow11 |  |
|  |  | 182 | - | 197 | Rainbow12 |  |
|  |  | 198 | - | 213 | Rainbow13 |  |
|  |  | 214 | - | 229 | Rainbow14 |  |
|  |  | 230 | - | 255 | Rainbow15 |  |
| 11 | Auto | 000 | - | 005 | No function | AUTO Program |
|  |  | 006 | - | 030 | Auto Program1 |  |
|  |  | 031 | - | 055 | Auto Program2 |  |
|  |  | 056 | - | 080 | Auto Program3 |  |
|  |  | 081 | - | 105 | Auto Program4 |  |
|  |  | 106 | - | 130 | Auto Program5 |  |
|  |  | 131 | - | 155 | Auto Program6 |  |
|  |  | 156 | - | 180 | Auto Program7 |  |
|  |  | 181 | - | 205 | Auto Program8 |  |
|  |  | 206 | - | 230 | Auto Program9 |  |
|  |  | 231 | - | 255 | Auto Program10 |  |
| 12 | Speed | 000 | - | 255 | Auto program speed slow->fast | Speed |
| 13 | Fade | 000 | - | 255 | Auto program Fade | Fade |
| 14 | Dimmer Curve | 000 | - | 005 | No function | Set dimmer curve |
|  |  | 006 | - | 063 | Linear Dimmer Curve |  |
|  |  | 064 | - | 127 | Exponential Dimmer Curve |  |
|  |  | 128 | - | 191 | Logarithmic Dimmer Curve |  |
|  |  | 192 | - | 255 | S-Curve Dimmer Curve |  |
| 15 | Device settings | 000 | - | 005 | No function | Device settings |
|  |  | 006 | - | 055 | Dimmer Response LED (Hold 3s) |  |
|  |  | 056 | - | 105 | Dimmer Response Halogen (Hold 5s) |  |
|  |  | 106 | - | 155 | Setting Fan High Mode (Hold 3s) |  |
|  |  | 156 | - | 205 | Setting Fan Auto Mode (Hold 3s) |  |
|  |  | 206 | - | 255 | Reset All Function(Hold 5s) |  |
| 16 | Ground Colour Dimmer | 000 | - | 255 | Ground Colour Dimmer 0%-100% | Ground Colour Dimmer |
| 17 | Ground Colour Strobe | 000 | - | 255 | Ground Colour Strobe slow->fast<1-20HZ | Ground Colour Strobe |
| 18 | Ground Colour Red | 000 | - | 255 | Ground Colour Red 0%-100% | Ground Colour Red |
| 19 | Ground Colour Green | 000 | - | 255 | Ground Colour Green 0%-100% | Ground Colour Green |
| 20 | Ground Colour Blue | 000 | - | 255 | Ground Colour Blue 0%-100% | Ground Colour Blue |
| 21 | Ground Colour Macro | 000 | - | 005 | Colour OFF | Ground Colour Macro |
|  |  | 006 | - | 013 | Red |  |
|  |  | 014 | - | 021 | Amber |  |
|  |  | 022 | - | 029 | Yellow Amber |  |
|  |  | 030 | - | 037 | Yellow |  |
|  |  | 038 | - | 045 | Green |  |
|  |  | 046 | - | 053 | Turquoise |  |
|  |  | 054 | - | 061 | Cyan |  |
|  |  | 062 | - | 069 | Blue |  |
|  |  | 070 | - | 077 | Lavender |  |
|  |  | 078 | - | 085 | Mauve |  |
|  |  | 086 | - | 093 | Magenta |  |
|  |  | 094 | - | 101 | Pink |  |
|  |  | 102 | - | 109 | Warm White |  |
|  |  | 110 | - | 117 | White |  |
|  |  | 118 | - | 125 | Cold White |  |
|  |  | 126 | - | 127 | Colour jumping stop |  |
|  |  | 128 | - | 191 | Colour jumping Speed slow->fast/Colour1->12 |  |
|  |  | 192 | - | 255 | Colour fading Speed slow->fast/Colour1->12 |  |

| 37Ch mode |
| --- |
| Ch. | Function | Values | Sub-group |
| 1 | Zoom | 000 | - | 255 | 0%-100% | Zoom |
| 2 | Zoom speed | 000 | - | 255 | Fast->Slow | Zoom speed |
| 3 | Dimmer | 000 | - | 255 | 0%-100% | Dimmer |
| 4 | Strobe functions | 000 | - | 005 | Strobe open | strobe |
|  |  | 006 | - | 010 | Strobe closed | Multifunctional-strobe |
|  |  | 011 | - | 033 | Pulse Random, slow->fast |  |
|  |  | 034 | - | 056 | Ramp up Random, slow -> fast |  |
|  |  | 057 | - | 079 | Ramp down Random, slow -> fast |  |
|  |  | 080 | - | 102 | Random Strobe Effect, slow -> fast |  |
|  |  | 103 | - | 127 | Strobe Break Effect, 5s…..1s (Short burst with break) |  |
|  |  | 128 | - | 250 | Strobe slow -> fast <1Hz - 20Hz |  |
|  |  | 251 | - | 255 | Strobe open |  |
| 5 | Red | 000 | - | 255 | Red 0%-100% | Red |
| 6 | Green | 000 | - | 255 | Green 0%-100% | Green |
| 7 | Blue | 000 | - | 255 | Blue 0%-100% | Blue |
| 8 | White | 000 | - | 255 | White 0%-100% | White |
| 9 | Colour Macro (override RGBW) | 000 | - | 005 | Colour OFF | Colour Macro |
|  |  | 006 | - | 013 | Red |  |
|  |  | 014 | - | 021 | Amber |  |
|  |  | 022 | - | 029 | Yellow Amber |  |
|  |  | 030 | - | 037 | Yellow |  |
|  |  | 038 | - | 045 | Green |  |
|  |  | 046 | - | 053 | Turquoise |  |
|  |  | 054 | - | 061 | Cyan |  |
|  |  | 062 | - | 069 | Blue |  |
|  |  | 070 | - | 077 | Lavender |  |
|  |  | 078 | - | 085 | Mauve |  |
|  |  | 086 | - | 093 | Magenta |  |
|  |  | 094 | - | 101 | Pink |  |
|  |  | 102 | - | 109 | Warm White |  |
|  |  | 110 | - | 117 | White |  |
|  |  | 118 | - | 125 | Cold White |  |
|  |  | 126 | - | 127 | Colour jumping stop |  |
|  |  | 128 | - | 191 | Colour jumping Speed slow->fast/Colour1->12 |  |
|  |  | 192 | - | 255 | Colour fading Speed slow->fast/Colour1->12 |  |
| 10 | Rainbow | 000 | - | 005 | Rainbow off | Rainbow effect |
|  |  | 006 | - | 021 | Rainbow1 |  |
|  |  | 022 | - | 037 | Rainbow2 |  |
|  |  | 038 | - | 053 | Rainbow3 |  |
|  |  | 054 | - | 069 | Rainbow4 |  |
|  |  | 070 | - | 085 | Rainbow5 |  |
|  |  | 086 | - | 101 | Rainbow6 |  |
|  |  | 102 | - | 117 | Rainbow7 |  |
|  |  | 118 | - | 133 | Rainbow8 |  |
|  |  | 134 | - | 149 | Rainbow9 |  |
|  |  | 150 | - | 165 | Rainbow10 |  |
|  |  | 166 | - | 181 | Rainbow11 |  |
|  |  | 182 | - | 197 | Rainbow12 |  |
|  |  | 198 | - | 213 | Rainbow13 |  |
|  |  | 214 | - | 229 | Rainbow14 |  |
|  |  | 230 | - | 255 | Rainbow15 |  |
| 11 | Auto | 000 | - | 005 | No function | AUTO Program |
|  |  | 006 | - | 030 | Auto Program1 |  |
|  |  | 031 | - | 055 | Auto Program2 |  |
|  |  | 056 | - | 080 | Auto Program3 |  |
|  |  | 081 | - | 105 | Auto Program4 |  |
|  |  | 106 | - | 130 | Auto Program5 |  |
|  |  | 131 | - | 155 | Auto Program6 |  |
|  |  | 156 | - | 180 | Auto Program7 |  |
|  |  | 181 | - | 205 | Auto Program8 |  |
|  |  | 206 | - | 230 | Auto Program9 |  |
|  |  | 231 | - | 255 | Auto Program10 |  |
| 12 | Speed | 000 | - | 255 | Auto program speed slow->fast | Speed |
| 13 | Fade | 000 | - | 255 | Auto Fade | Fade |
| 14 | Dimmer Curve | 000 | - | 005 | No function | Set dimmer curve |
|  |  | 006 | - | 063 | Linear Dimmer Curve |  |
|  |  | 064 | - | 127 | Exponential Dimmer Curve |  |
|  |  | 128 | - | 191 | Logarithmic Dimmer Curve |  |
|  |  | 192 | - | 255 | S-Curve Dimmer Curve |  |
| 15 | Device settings | 000 | - | 005 | No function | Device settings |
|  |  | 006 | - | 055 | Dimmer Response LED (Hold 3s) |  |
|  |  | 056 | - | 105 | Dimmer Response Halogen (Hold 5s) |  |
|  |  | 106 | - | 155 | Setting Fan High Mode (Hold 3s) |  |
|  |  | 156 | - | 205 | Setting Fan Auto Mode (Hold 3s) |  |
|  |  | 206 | - | 255 | Reset All Function(Hold 5s) |  |
| 16 | Red1 | 000 | - | 255 | Red1 0%-100% | Red1 |
| 17 | Green1 | 000 | - | 255 | Green1 0%-100% | Green1 |
| 18 | Blue1 | 000 | - | 255 | Blue1 0%-100% | Blue1 |
| 19 | White1 | 000 | - | 255 | White1 0%-100% | Whtie1 |
| 20 | Red2 | 000 | - | 255 | Red2 0%-100% | Red2 |
| 21 | Green2 | 000 | - | 255 | Green2 0%-100% | Green2 |
| 22 | Blue2 | 000 | - | 255 | Blue2 0%-100% | Blue2 |
| 23 | White2 | 000 | - | 255 | White2 0%-100% | Whtie2 |
| 24 | Red3 | 000 | - | 255 | Red3 0%-100% | Red3 |
| 25 | Green3 | 000 | - | 255 | Green3 0%-100% | Green3 |
| 26 | Blue3 | 000 | - | 255 | Blue3 0%-100% | Blue3 |
| 27 | White3 | 000 | - | 255 | White3 0%-100% | Whtie3 |
| 28 | Red4 | 000 | - | 255 | Red4 0%-100% | Red4 |
| 29 | Green4 | 000 | - | 255 | Green4 0%-100% | Green4 |
| 30 | Blue4 | 000 | - | 255 | Blue4 0%-100% | Blue4 |
| 31 | White4 | 000 | - | 255 | White4 0%-100% | Whtie4 |
| 32 | Ground Colour Dimmer | 000 | - | 255 | Ground Colour Dimmer 0%-100% | Ground Colour Dimmer |
| 33 | Ground Colour Strobe | 000 | - | 255 | Ground Colour Strobe slow->fast<1-20HZ | Ground Colour Strobe |
| 34 | Ground Colour Red | 000 | - | 255 | Ground Colour Red 0%-100% | Ground Colour Red |
| 35 | Ground Colour Green | 000 | - | 255 | Ground Colour Green 0%-100% | Ground Colour Green |
| 36 | Ground Colour Blue | 000 | - | 255 | Ground Colour Blue 0%-100% | Ground Colour Blue |
| 37 | Ground Colour Macro | 000 | - | 005 | Colour OFF | Ground Colour Macro |
|  |  | 006 | - | 013 | Red |  |
|  |  | 014 | - | 021 | Amber |  |
|  |  | 022 | - | 029 | Yellow Amber |  |
|  |  | 030 | - | 037 | Yellow |  |
|  |  | 038 | - | 045 | Green |  |
|  |  | 046 | - | 053 | Turquoise |  |
|  |  | 054 | - | 061 | Cyan |  |
|  |  | 062 | - | 069 | Blue |  |
|  |  | 070 | - | 077 | Lavender |  |
|  |  | 078 | - | 085 | Mauve |  |
|  |  | 086 | - | 093 | Magenta |  |
|  |  | 094 | - | 101 | Pink |  |
|  |  | 102 | - | 109 | Warm White |  |
|  |  | 110 | - | 117 | White |  |
|  |  | 118 | - | 125 | Cold White |  |
|  |  | 126 | - | 127 | Colour jumping stop |  |
|  |  | 128 | - | 191 | Colour jumping Speed slow->fast/Colour1->12 |  |
|  |  | 192 | - | 255 | Colour fading Speed slow->fast/Colour1->12 |  |